## Slide 1
01

## Slide 2
Automatic Lesion Segmentation Method on Mammograms Using Deep Learning Patch-Based Techniques
Key words: patch extraction, Unet, mamography, deep learning, segmentation
02

## Slide 3
Members:
1. Mai Tat Chuyen – 20213683
2. Trinh Khanh Ly – 20213676
3. Ong Thi Huyen Trang – 20213683
Instructor: PhD. Nguyen Viet Dung
03

## Slide 4
Content:
1. Introduction
2. Related works
3. Methodology
4. Experiment
5. Result and Evaluation
6. Discusion
7. Conclusion
8. References
04

## Slide 5: 1. Introduction
1.1 Overview of Breast Cancer
The most common cancer in women globally [1]
High mortality rates, especially in developing countries [2]
In Vietnam in 2022, among female cancers, breast cancer has the highest incidence rate at 28.9%, with approximately 24,563 new cases, resulting in 10,008 deaths [3]
The use of imaging diagnostic tools for regular screening to detect diseases at an early stage is crucial.
Tỷ lệ các ca mắc ung thư mới ở nữ giới tại Việt Nam theo Globocan 2022
05

## Slide 6: 1. Introduction
1.2. Mammography:
A quick, non-invasive, and cost-effective method for screening breast cancer
Utilizes X-ray imaging to visualize breast tissue.
Two common applications are screening mammography and diagnostic mammography.
06

## Slide 7: 1. Introduction
1.3. Lesions on Mammographic Images
- Calcification
Mass lesions: characterized by various attributes:
Shape (round, lobulated, oval, irregular) [4]
Margins (well-defined, ill-defined, or spiculated)
Size
Location
Contrast
- Detecting mass lesions is more challenging than calcifications due to their similarity and ambiguity in characteristics compared to normal tissue [5]
07

## Slide 8
1.4 Importance of Early Detection of Breast Cancer:
Early detection of breast masses reduces the mortality rate by 20% (in the United States) and allows for curative treatment. Reduces treatment costs and time.
Early detection can ensure aesthetic outcomes.
1.5 Challenges for doctors in Diagnosis:
Difficulty in interpretation due to the complex structure
of the breast.
Overlapping structures may obscure abnormal findings.
1. Introduction
08

## Slide 9: 1. Introduction
1.6 System diagram :
09

## Slide 10: 2. Related works
2.1 The UNet architecture [6]
UNet: CNN architecture for segmentation.
Resembles letter "U".
Encoder extracts features.
Two convolutional layers per block.
ReLU activation used.
Max pooling downsamples features.
10

## Slide 11: 2. Related Works
2.2 EfficentNet [7]
Introduced in the paper "EfficientNet: Rethinking Model Scaling for Convolutional Neural Networks" by Mingxing Tan and Quoc V. Le in 2019
The EfficientNet family includes several models (EfficientNet-B0 to EfficientNet-B7)
11

## Slide 12: 2. Related Works
2.3 Unet backbone EfficentNet B7 [7]
EfficientNet B7 has a large, high performance parameter set
-> helps improve feature extraction performance on patches
12

## Slide 13: 2. Related work
160x112x32
Input Image
Block4
Block6
Block7
Block5
Block3
Block2
Up-Conv2D
Concat
Concat
Output Image
Conv2D
Conv2D
Block1
Up-Conv2D
Up-Conv2D
Concat
Up-Conv2D
Concat
Up-Conv2D
320x224x3
80x56x48
40x28x80
20x14x80
20x14x224
10x7x384
10x7x640
20x14x512
40x28x256
80x56x128
160x112x64
320x224x16
320x224x7
Block 1: 4 MBConv1 blocks, k=3
Block 2: 7 MBConv6 blocks, k=3
Block 3: 7 MBConv6 blocks, k=5
Block 4: 10 MBConv6 blocks, k=3
Block 5: 10 MBConv6 blocks, k=5
Block 6: 10 three MBConv6 blocks, k=5
Block 7: 4 MBConv6 blocks, k=3
The UNet model architecture with EfficientNet0-B7 backbone proposed by B. Baheti.
13

## Slide 14: 2. Related work
2.4 Patch extraction
By Shen et al., in mammogram images, the regions containing lesions usually represent only a small part of the image ( 0.08% of image)  full image hard to train
By Quintana et al. [8], patch-based methods directly exploit lesion-level annotations by first training on patches, then extending it to a whole image classifier
Has been demonstrated to be effective in previous studies [8]
There is no single patch size or resolution that is optimal for all lesion sizes and types [8]
Patch extraction
(blue square)
14

## Slide 15: 3. Methodology
3.1 Proposed model: Unet backbone Efficient Net B7
Input Image
Block4
Block6
Block7
Block5
Block3
Block2
Up-Conv2D
Concat
Concat
Output Image
Conv2D
Conv2D
Block1
Up-Conv2D
Up-Conv2D
Concat
Up-Conv2D
Concat
Up-Conv2D
16

## Slide 16: 3. Methodology
3.1 Proposed model: Unet backbone Efficient Net B7
Why using skip connection between image and mask output?
Advantage[11],[12]:
Increase model complexity, Overcome loss of information from encoder to decoder
 Should be used with large amounts of data
Reduces vanishing gradient phenomenon, making model training easier
Disadvantage:
Increases model complexity as well as the risk of overfitting
Reducing resources may be acceptable to increase performance
Useful when data is highly homogeneous [13] and careful combination of global and local information is required  Suitable for Mammography image [13]
The use of Skip connection should be considered
17

## Slide 17: 4. Experiment
4.1. Dataset
4.1.1. Curated Breast Imaging Subset of Digital Database for Screening Mammography (CBIS – DDSM)
DDSM is a well-known database of mammographic images.
CBIS-DDSM is an updated and standardized version of DDSM consisting of 2620 studies, containing cases of normal, benign, and malignant lesions with verified pathology information.
X-ray images with tumor sizes larger than 1024 × 1024 pixels are not used.
A total of 1507 images were selected from all mammographic images with tumors in the CBIS-DDSM dataset.
18

## Slide 18: 4. Experiment
4.1.2. INBreast
Collected at Centro Hospitalar de S. Joao, Breast Center, Porto with the permission of the Portuguese National Data Protection Commission.
Fully digital imaging equipment (in contrast to digitized X-ray imaging from film).
Data collected from August 2008 to July 2010, INBreast comprises a total of 115 cases with a total of 410 images.
The dataset includes various types of lesions: masses, calcifications, asymmetries, and distortions. Roi mask images, annotated by experts, are also provided in XML format.
4.1. Dataset
19

## Slide 19: 4. Experiment
4.2 Preprocessing
Step 1: Normalize the image set to 8-bit PNG format.
Step 2: Flip the images entirely to the left.
Step 3: Remove digitization errors. The cropping ratio is chosen as 4% of the image length for both the top and bottom edges; 1% of the image width for the left edge. Crop similarly for the Roi mask images.
Step 4: Remove image labels and noisy components.
Fig. Some images after preprocessing
20

## Slide 20: 4. Experiment
4.3 Patch extraction from original images
Patches are extracted from the original image with specific size and stride to ensure no information is missed.
3 type of patch size
1024 x 1024 , stride = 128
512 x 512 , stride = 64
256x256 , stride = 64
Bảng thống kê độ biến thiên kích thước ảnh và BB
 | Width (pixel) |  | Length | 
 | Minimum | Maximum | Minimum | Maximum
Image | 3608 | 6308 | 994 | 5323
Bounding box | 112 | 946 | 51 | 1006
21
BB size | a,b < 200 | (200<a<450)&(b<450) (200<b<450)&(a<450) | Others
Patch size | 256x256 | 515x512 | 1024x1024
Stride | 64 | 64 | 250

## Slide 21: 4. Experiment
4.3 Patch extraction from original images
Extract patch containing mass
The number of pixels is 1 in the ROI image
= The number of pixels is 1 in the mask image
Label: Mask contains mass
Extract the same location
The extracted sample patches have an intersection degree (IoU) of less than 0.5 between each other
22

## Slide 22: 4. Experiment
4.3 Patch extraction from original images
Extract patch that does not contain mass
The number of pixels 1 is 0
Mask does not contain mass
The number of pixels 1
is different from 0
< 0.5 % of image area
Patch contains normal breast tissue
Keep data imbalance
23

## Slide 23: 4. Experiment
Total number of images after extracting the patch
 | Number of Images | Type | Number of patches | Total
Training Set | 1104 | Image | 30633 | 61266
 |  | Mask | 30633 | 
Validation Set | 285 | Image | 5066 | 10132
 |  | Mask | 5066 | 
Test Set | 118 | Image | 2835 | 5670
 |  | Mask | 2835 | 
24

## Slide 24: 5. Result and evaluation
5.1 Evaluation metrics
25

## Slide 25: 5. Result and evaluation
5.2 Training process
Parameter, Method | Value
DL frameworks | Tensorflow
Batch size | 32
Learning rate | 1e-4
Lossfunction | Binary crossentropy
Number of epochs | 60
Optimizer | Adam
Pretrained weight | ImageNet
 | CBIS-DDSM |  | INBreast | 
 | Dice score | IoU score | Dice score | IoU score
Standard Unet [9] | 78.62 | 64.87 | 89.21 | 79.5
Connected-Unets [9] | 82.22 | 69.82 | 93.36 | 85.75
AUNet [10] | 90.47 | 82.65 | 94.45 | 89.72
Unet-Efficient B7 | 90.24 | 85.36 | 94.82 | 90.04
Unet-Efficient B7* (Proposed model) | 90.81 | 86.17 | 94.56 | 90.43
26

## Slide 26: 6. Discussion
A high IoU indicates that the model is capable of segmenting tumor regions with a fairly good match rate between predicted and actual.
--> the overall performance of the model in correctly identifying the tumor region.
Dice Score lower than UNet-EfficientB7 shows that, although the area between predicted and actual is good, there is a large difference in the total number of pixels in the predicted area and the actual area.
Because the model predicts regions that are larger/or smaller than they actually are, this leads to differences in size and shape.
28

## Slide 27: 5. Result and evaluation
27
- Red line: ground truth,
- Green line: segmentation from model 1,
- Blue line: segmentation from model 2
5.3. Image segmenting some patches containing masses
Some patches containing masses where model 1 detected the masses, but model 2 did not detect the masses
Some patches containing masses where model 2 detected the masses, but model 1 did not detect the masses

## Slide 28: 7. Conclusion
The method of extracting patches containing mass and not containing mass helps enhance image data for model training and testing
The EfficientNet-B7 UNet backbone model with skip connection between image- mask trained on patches of mamography images gives good segmentation results.
Improve tumor image segmentation performance.
Has potential applications with screening, diagnostic for breast cancer on mammograms
29

## Slide 29: 8. References
[1] Freddie Bray et. al., "Global Cancer Statistics 2022: GLOBOCAN Estimates of Incidence and Mortality Worldwide for 36 Cancers in 185 countries,"A Cancer Journal for Clinicians, vol. 74, pp. 229-263 (2024).
[2] 900-world-fact-sheet.pdf (who.int)
[3] 704-viet-nam-fact-sheet.pdf (who.int)
[4] . S. a. B. Nagarajanb, "Automatic diagnosis of mammographic abnormalities based on hybrid features with learning classifier," January 2012.
[5] S. M. R. M. B. K. M. I. Afsaneh Jalalian, "Foundation and methodologies in computer-aided diagnosis systems for breast cancer detection”," EXCLI J, p. 16: 113–137, 2017.
[6] P. F. a. T. B. Olaf Ronneberger, "U-Net: Convolutional Networks for Biomedical Image Segmentation," MICCAI, 2015.
[7] Q. V. L. Mingxing Tan, "EfficientNet: Rethinking Model Scaling for Convolutional Neural Networks," International Conference on Machine Learning, 2019.
[8] Quintana, Gonzalo Iñaki, et al. "Exploiting Patch Sizes and Resolutions for Multi-Scale Deep Learning in Mammogram Image Classification." Bioengineering, vol. 10, no. 5, 2023, p. 534,
[9] Baccouche A, Garcia-Zapirain B, Castillo Olea C, Elmaghraby AS. Connected-UNets: a deep learning architecture for breast mass segmentation. NPJ Breast Cancer. 2021 Dec 2;7(1):151. doi: 10.1038/s41523-021-00358-x. PMID: 34857755; PMCID: PMC8640011.
[10] Alkhaleefah, Mohammad, et al. "Connected-SegNets: A Deep Learning Model for Breast Tumor Segmentation from X-ray Images." Cancers, vol. 14, no. 16, 2022, p. 4030.
[11] Xu, Guoping, et al. "Development of Skip Connection in Deep Neural Networks for Computer Vision and Medical Image Analysis: A Survey." Wuhan Institute of Technology, Wuhan, Hubei, China, 430205. Wuhan University, Wuhan, Hubei, China, 430072
[12] Lachinov, Dmitrii, et al. "Projective Skip-Connections for Segmentation Along a Subset of Dimensions in Retinal OCT." Medical Imaging.
[13] Chang, Tien-Yu, et al. "Three-layer Heterogeneous Mammographic Phantoms for Monte Carlo Simulation of Normalized Glandular Dose Coefficients in Mammography." Breast Dosimetry for Mammography.
30

## Slide 30
THANK YOU FOR YOUR LISTENING!